## Slide 1: Current understanding of tokamak plasma eruption control and the consequences for ITER
Joe Allen, JOA509

## Slide 2: Talk Outline
Background understanding of type-I Edge Localised Modes (ELMs)
Problems ELMs cause & ITER’s requirements
Methods for ELM control on ITER
  Resonant magnetic perturbations (RMPs)
  Pellet injection
  Vertical kicks
Alternatives

## Slide 3: 1. Background understanding of ELMs
Generic to tokamaks in H-mode
Edge pedestal gradient is inherently unstable
Thought to be caused by Peeling-Ballooning mode instabilities
  ELM causes crash, cycle repeats
H. Wilson Plas. Phys. 48 2006
Type-I ELM cycles

## Slide 4: 1. Background understanding of ELMs
Several tokamaks have corroborated this scaling for ELM frequency, fELM
∆WELM is the ELM energy
A. Leonard Journal of Nuclear Materials 266 1999
Notes: Quick slide!

## Slide 5: 2. Problems ELMs cause
Loss of confinement
High heat flux expelled from the plasma
  Can cause critical damage to PFCs
May destabilise core plasma modes
However they reduce plasma impurity levels

## Slide 6: 2. ITER’s requirements
Natural ELMs on ITER could release up to 20 MJ
  The first wall can tolerate < 1 MJ eruptions
Minimum ELM frequency increase to maintain acceptable impurity levels and sufficient PFC lifetime, depending on plasma current.
Target operation: 15 MA
  AT LEAST need a sustained >40 times fELM increase
A. Kirk Phys. Rev. Lett. 108.25 2013

## Slide 7: 3. Methods for ELM control on ITER
Vertical stability coils already included
27 RMP coils added to design
Pellet injectors also added
P. Lang Nuclear Fusion 53.4 2013
Notes: Quick slide!

## Slide 8: 3. i) RMPs (Resonant Magnetic Perturbations)
Suppress ELMs by keeping below PB stability limit
Small perturbations ≈ 10-4 T
Perturbations must be toroidally cycled to keep divertor damage uniform
A Kirk Frontiers Lectures 2016
Notes: Complete suppression is ideal
Small perturbations disrupt toroidal symmetry
  Divertor heat loads become non uniform  perturbations must be varied around tokamak or mode number changed to even out this divertor degradation
Not always achievable  Parameters for RMP success need to be calculated in ITER’s early operation

## Slide 9: 3. ii) Pellet Injection (PI)
Mitigation by increasing f_ELM  less damage to PFCs
Mechanism not fully understood
Heavily dependent on time since
last ELM
I. Chapman Plas. Phys. Cont. Fus. 58 1 2016
Control by pacing the frequency of ELMs
Vertical stability coils
Plasma moves ≈ 2% of minor radius
iii) Vertical Kicks (VKs)
Notes: Non-resonant effect so can be used at all times throughout at discharge
Thought to be caused by ablation of pellet in pedestal region  increasing local pressure above ballooning stability limit and provoking an ELM
Can cause over-fuelling of the plasma which reduces fusion performance

## Slide 10
2nd: Partial RMP suppression + VK/PI mitigation
3rd: Sustained VK/PI mitigation with fELM above threshold
1st: Complete, sustained RMP suppression
Notes: Likely will need some small ELMs to control core impurity levels  unless alternatives can be found to increase internal transport

## Slide 11: 4. Alternatives
QH-mode or I-mode
  High fusion performance without ELMs!
    (but with enhanced transport!)
Sounds worth investigating
Notes: Sounds worth investigating, if not for ITER then at least for the next generation of tokamaks
Control techniques discussed don’t work in every scenario  need something more robust
  A new, more stable operating regime would be ideal for a fusion power plant

## Slide 12: Thank you for listening!