## Slide 1: Current understanding of tokamak plasma eruption control and the consequences for ITER
Joe Allen, JOA509

## Slide 2: Talk Outline
Background understanding of type-I Edge Localised Modes (ELMs)
Problems ELMs cause & ITER’s requirements
Methods for ELM control
  Resonant magnetic perturbations (RMPs)
  Pellet injection
  Vertical kicks
ELM control on ITER

## Slide 3: 1. Background understanding of ELMs
Generic to tokamaks in H-mode
Edge pedestal gradient is inherently unstable
Thought to be caused by Peeling-Ballooning mode instabilities
  ELM causes crash, cycle repeats
H. Wilson Plas. Phys. 48 2006
Type-I ELM cycles

## Slide 4: 1. Background understanding of ELMs
Several tokamaks have corroborated this scaling for ELM frequency, fELM
∆WELM is the ELM energy
A. Leonard Journal of Nuclear Materials 266 1999

## Slide 5: 2. Problems ELMs cause
Loss of confinement
High heat flux expelled from the plasma
  Can cause critical damage to PFCs
May destabilise core plasma modes
However they reduce plasma impurity levels

## Slide 6: 2. ITER’s requirements
Minimum ELM frequency increase to maintain acceptable impurity levels and sufficient PFC lifetime, depending on plasma current.
Target operation: 15 MA
  AT LEAST need a sustained >40 times fELM increase
A. Kirk Phys. Rev. Lett. 108.25 2013

## Slide 7: 3. Methods for ELM control
RMP – suppress ELMs by keeping below PB stability limit
PI & VK – mitigation by increasing f_ELM  less damage to PFCs
ITER coil layout pic

## Slide 9: 4. ELM control on ITER
Vertical stability coils already included
27 RMP coils added to design
Pellet injectors also added
P. Lang Nuclear Fusion 53.4 2013

## Slide 10
2nd: Partial RMP suppression + VK/PI mitigation
3rd: Sustained VK/PI mitigation with fELM above threshold
1st: Complete, sustained RMP suppression

## Slide 11: 4. ELM control on ITER